## Slide 1
Optimizing Tracking Windows for Improved Cislunar Inter-Satellite Autonomous Navigation
Student
Thomas Bosboom
Supervisors
Stefano Speretta
Erdem Turan
Notes: Thank you all for being here
First, supervisors Stefano Speretta and Erdem Turan for providing great tips and tricks through the last year, related to the topics of the thesis, but also programming and the prioritization of certain aspects of the work.
Of course, I also would like to thank my friends and family for their support over the year.
Topic: Optimizing Tracking Windows for Improved Cislunar Inter-Satellite Autonomous Navigation
This topic may seem very futuristic to some, but it is quite relevant in today’s space industry. In fact, for the next 30 minutes I hope to provide to you:
Good overview of current developments in navigation in cislunar space
Research gabs
What way my thesis work provides benefits to future missions related to autonomous inter-satellite navigation in the cislunar environment
NEXT SLIDE

## Slide 2
Scientific context
Notes: To get everyone on the same page, let's go over the scientific context.

## Slide 3: Scientific context | Current trends
    Small satellites “SmallSats” (<500kg):
        Low cost, offering more space-based services
        Mostly around Earth (LEO)
Notes: In this work I talk in the context of small satellites/”smallsats”.
Over the years smallsats have become increasingly popular for a variety of space applications due to their low cost, versatility and compact size, driven by improved COTS subsystems. Especially when these developments in the miniaturization and cost reduction of spacecraft systems are combined with the availability of lower cost launchers, it paves the way for increased academic and economic interest.
Most of those satellites reside in orbits around the Earth, predominantly LEO.
NEXT SLIDE

## Slide 4: Scientific context | Current trends
    Small satellites “SmallSats” (<500kg):
        Growing demand for missions beyond Earth
        Mostly cislunar space
Notes: However, recent developments show that there is a growing technical and economic interest for space missions beyond Earth, of which most are focussed on missions in cislunar space: defined as the volume of space predominantly influenced by the gravity of Earth and/or Moon.
The demand is mostly driven by the potential of in-situ resource utilization, human exploration and understanding of the history of the solar system.
NEXT SLIDE

## Slide 5: Scientific context | Cis-lunar navigation
      Problem
        Reliance on ground-based tracking:
          Crowded networks
          Expensive operationally
          Less data sent
      Solution: inter-sat autonomous navigation
        Lower operational costs
        Used with existing radio technologies
        Can be used in many scenarios
Notes: Unfortunately, we can’t just launch a satellite into space and hope for the best.
To be successful: pos and vel: orbit determination or tracking.
Based on this, SKMs to planned trajectory: navigation and control.
The conventional approach to OD; send signals back and forth to the spacecraft, such as the Deep Space Network (DSN). (Left figure).
However:
Increasing number of launched small satellites is a stressing factor on the existing communication networks in terms of communication availability, which exerts pressure on the orbit determination process and ultimately the financial budget and consequently maybe scientific yield of a small satellite mission.
Another limitation is that comms with Earth ground station requires a direct line of sight, which is not always possible for some satellite orbits and lunar assets on the polar and far-side regions of the moon.
Instead: comms link between at least two bodies. In certain configuration where there is at least one orbit that have a unique size, shape, and orientation due to asymmetric acceleration environment, it is possible to simultaneously obtain their absolute position and velocity information simultaneously using relative observations such as range or range-rate.
AOD benefits:
Lower operational cost by not using DSN as much.
Used with existing radio technologies that are used on-board spacecraft today. Because already existing COTS products can be used for this, it can lead to lower cost no further dev costs.
Less delays in manoeuvres. related to DTE comms, since these spacecraft operate autonomously, there is less need for commands to be send back and forth Earth for processing.
Provide navigation services to lunar surface assets which are not in the line of sight with earth.
NEXT SLIDE

## Slide 6: Scientific context | Research gap
    Literature:
        Autonomous navigation, but assumes continuous tracking
        Tracking optimization
          But with Earth communications
          With AOD but not related to design budgets
      Exploratory study:
        Explore whether one can minimize scheduling based on a design budget:
        Explore operational and design implications
Notes: Concept of inter-satellite navigation is not new. But subtopics are not well connected with each other or offer solutions that are not as practical during actual operations. For example,
Intersatellite orbit determination is done but it assumes that two spacecraft perform a tracing session for a long period of time. For example, some research consider tracking for 14 days, which is not realistic from an operational standpoint because a mission is not only OD and navigation but also has mission objectives related to its payload. Therefore, there are gaps between tracking sessions. These tracking arcs can be optimized.
This timing optimization has been done predominantly for DTE in other literature.
The limited studies that do look at the tracking timing with ISLs only look at the estimation uncertainty aspect and don’t include calculations relevant for design budgets that might be useful for the design or whole mission of a spacecraft.
In order to fill these research gaps, this work aims to relate autonomous inter satellite navigation with useful parameters for mission design.
One such parameters is station keeping costs, defined as deltav. I specifically look at how this can be reduced by finding the best set of time windows in which tracking is performed.
Based on this results, my thesis work then also aims to provide insights about how deploying those timing solutions can be relevant from an operational and design perspective.
NEXT SLIDE

## Slide 7
Research question
What is an optimal satellite-to-satellite tracking timing configuration for cislunar orbiters?
Notes: As such, the research question can be defined as the following:

## Slide 8
Methodology
Notes: Before I go the results, it is important to gain a clear understanding of:
what satellite constellation we are dealing with
how the OD and navigation process actually works
Test setup
NEXT SLIDE

## Slide 9: Methodology | LUMIO-LPF case study
      Lunar Meteoroid Impact Observer (LUMIO)
        Orbit: southern L2 Lagrange point
        Objective:
          Detect meteors on lunar far-side
          Demonstrate autonomous navigation (optical)
        Operations: 1 year
        Small sat (approx. 23 kg)
      SSTL Lunar Pathfinder (LPF)
        Orbit: Elliptical Lunar Frozen Orbit
        Objective:
          Contribute to ESA Moonlight
          Communication relay satellite covering lunar poles and far-side
        Operations: 8 years
        Small sat (approx. 280 kg)
Notes: Case study:
Two satellites, LPF and LUMIO: both smallsats
Config of short period with large separation distances has state observability, which is a metric that describes how easy it is to estimate the states with OD.
LPF:
Orbits closely around the Moon in a very elliptical orbit.
Relay to provide coverage of the hard-to-contact places on the lunar surface, which are the poles and far-side.
Part of ESA’s Moonlight initiative, to develop dedicated telecommunications and navigation services for the Moon.
LUMIO:
L2 Lagrange point behind the moon
Detect light flashes from meteor impacts on the far side of the Moon.
This is a project that TU Delft has close ties with as well, in collaboration with Politecnico di Milano and ESA.
Mission lifetime of 1 year and will be relevant to the optimization later on.
LPF orbit is much more stable than the L2 as LUMIO’s orbit is more susceptible to perturbation forces: simplify the optimization to one satellite only, we will only look at the cost reduction of SKMs of LUMIO.
NEXT SLIDE
In this work I looked at one particular case study, which is a hypothetical constellation that exists out of two satellites, LPF and LUMIO. This combination was chosen is not only because these are smallsats but also because literature has shown that the relative orbit geometry in such a configuration has shown to be great in terms of state observability, which is a concept that describes how easy it is to estimate the states.
The first is the LPF, which has an orbit that orbits closely around the Moon in a very elliptical shape. This is a satellite built by the British company Surrey Satellite Technologies (SSTL) with the aim to provide coverage of the hard-to-contact places on the lunar surface, which are the poles and far-side, and to serve as a relay satellite to redirect information of those lunar assets back to Earth. It is also part of ESA’s Moonlight initiative, to develop dedicated telecommunications and navigation services for the Moon.
The second is LUMIO, which is a satellite that moves in an L2 Lagrange point behind the moon, as its main mission objective is to detect light flashes from meteor impacts on the far side of the Moon. This is a project that TU Delft has close ties with as well, in collaboration with Politecnico di Milano and ESA. The most important aspect of remember is that it has a mission lifetime of 1 year and will be relevant to the optimization later on.
The most important thing to remember that LPF orbit is much more stable than the L2 as LUMIO’s orbit is more susceptible to perturbation forces. For that reason, and to simplify the optimization to one satellite only, we will only look at the cost reduction of SKMs of LUMIO.

## Slide 10: Methodology | LUMIO’s orbit
Notes: In order to get a better understanding of what LUMIO’s orbit should look like, this video gives a nice visual representation. You can clearly see that the orbit should remain in a halo-like shape which explains why those LPO’s are also called halo-orbits.
NEXT SLIDE

## Slide 11: Methodology | LUMIO-LPF case study
Notes: Here is visual representation to give you a better sense of the relative orbital geometries. Blue is the LPO, red the ELO. In the inertial frame, you can see the small orbit of LPF orbiting the Moon and the blue LUMIO orbit always moving further from Earth than the Moon itself.
You can see that LUMIO always covers up and down behind the Moon from the perspective of Moon and thus LPF. You can also see that the orbit of LPF is much smaller and changes orientation a lot. In short, this allows for many vantage points between the satellites.
NEXT SLIDE

## Slide 12: Methodology | LUMIO-LPF case study
Notes: You saw that the structure is still maintained, but gravitational pulls and other perbutational forces eventually distort its quasi-periodic structure. It clearly shows the need for a set of corrective manoeuvres within a (28-day period) to be able to sustain the periodic structure.
NEXT SLIDE

## Slide 13: Methodology | Navigation process
    ISL: range-only
    Arc: Weighted Least Squares
Notes: But how are the station keeping costs calculated?
In this figure, you can see a simplification on the problem. An ISL is performed in we will call a tracking arc that has a certain length or duration. After each tracking arc, a new estimation of the spacecraft position and velocity is found using the BLS estimator. It compares its currently be known state to where it should be at a point in the future and LUMIOs thrusters push it towards the right direction. It is assumed that the on-board computer directly calculates the required correction to keep LUMIO to the reference trajectory.
The total is then summed up. This total deltaV will then be used as the metric that will be optimized.
NEXT SLIDE

## Slide 14: Methodology | Navigation process | Baseline scenario
    ISL: range-only
    Arc: Weighted Least Squares
Notes: But in order to compare this metric, a baseline scenario is set up.
An initial tracking window configuration is defined as a set of tracking arcs with a length of 1 day combined with a 3-day interval between each arc, which equates to a station keeping frequency of 4 days. The simulation starts at MJD60390 and runs for 28 days.
Choice for this timing configuration is based on a suggestion in literature which states that performing 3 to 4 corrections per orbital period is the best for ∆V in LPOs.
A simulation of 28 days instead of 365 days is chosen due to memory and run time limitations. The 28-day duration covers two full LUMIO orbital periods which was deemed sufficient to represent costs for the full mission duration.
NEXT SLIDE

## Slide 15
What is an optimal* tracking satellite-to-satellite timing strategy for cislunar orbiters?
(Near) optimal:
Model details in the appendix
Notes: This baseline is compared to other configurations of tracking arcs and lengths as shown here.
What constitutes as a better solution is defined whether the total deltav of the individual orbit corrections are lower than the baseline. This will yield a NEAR OPTIMAL solution, rather than the true most optimal solution because due to the stochastic nature of the problem, is challenging to find the one and only perfect optimal solution.
Since the deltav relies on the magnitude of estimation errors from the OD process and previous corrections, which in turn depend on the relative geometry of the orbits during a tracking arc, solving for lowest ∆V is a complex optimization problem.
NEXT SLIDE

## Slide 16
Results
Notes: With the test cases of the tracking configurations in mind, lets look at the results.

## Slide 17
Results
Navigation analysis
Baseline scenario
Notes: For a nice flow, lets first look at the baseline scenario such that you have a better understand of what is happening in the simulation.

## Slide 18: Baseline scenario | Layout
Run of 28 days
Notes: The figure provides a graphical representation of the observations that occur over a period of 28 days. The arrows represent the magnitude and direction of the maneuvers. Note how the geometry explored by LPF neatly distributes over time. Additionally, note how an arc duration of 1 day captures the geometric diversity gained over a bit more than 2 LPF orbits. This suggest that an arc duration of 1 day likely provides more than enough geometrical information to sufficiently converge the estimator to an improved solution for the state estimate. As such, this could suggest the possibility of reducing the duration of each arc.

## Slide 19: Results | Default scenario | Relationships errors and
    Total annual
        0.6130.0066 1 m/s
      Dispersion: distance true trajectory and reference trajectory
      Estimation errors reduce for all states
    Total annual
        0.6130.0066 1 m/s
      Dispersion: distance true trajectory and reference trajectory
      Estimation errors reduce for all states
      Estimation errors < dispersion errors
        Reduce tracking time later on?
Notes: For this baseline scenario we find that the total annual deltaV is around 0.6 m/s. On the figure on the right, you can see a few interesting things.
Upper subfigure: individual corrections of which you can see that it occurs right after each tracking arc.
Estimation error goes down quite nicely to the lower bound defined by the noise characteristics of the observations.
Dispersion is a few orders of magnitude larger than the estimation error. This means that over a longer period of lime, the dispersion error is likely a much larger contributor to the total deltaV that the estimation. As such there might be a possibility to reduce the tracking time later on to do a correction earlier such that the dispersion has grown less in the meanwhile.
NEXT SLIDE

## Slide 20
Results
Navigation analysis
Candidate scenarios
Notes: With the previously given value for deltaV as a baseline, we are looking for improved solutions.
I will be discussing the outcomes of the analysis in which I look at different timing configurations to see which one performs best.
In the end, I will give an overview that compares the results of the three different categories discussed in the methodology.
NEXT SLIDE

## Slide 21
    In what way can one structure tracking arcs?
    Category 1: Constant timing
        Constant arc length and interval
        Easiest planning-wise
    Category 2: Orbit-based
        Specific locations in orbit, i.e. apolune and perilune of LPF
          Estimation accuracy depends on speed of the dynamics
      Category 3: Heuristic optimization based
        Individually adjusted arcs
Results | Candidate scenarios | Timing configurations
Notes: New that we have established how the deltaV is calculated For the baseline, we can compare different tracking window configurations.
A methodology was set up that aimed to compare three different timing strategy categories for which tracking can be performed with varying levels of complexity:
tracking based on constant tracking duration and interval: easiest to do, most intuitive and easy to plan
tracking around the perilune or apolune of the LPF satellite: Orbit-based tracking is based on the knowledge that passes in regions of faster dynamics (perilune) yield larger observability for position states and lower observability for velocity states. The opposite is true for apolune. What this means is that it might be more beneficial to perform tracking sessions at perilune to estimate position states and at perilune to estimate velocity states.
tracking based on the solution of a heuristic optimization routine that adjusts each tracking arc individually.
NEXT SLIDE

## Slide 22: Results | Candidate scenarios | Timing configurations
    First Constant and Orbit-based (categories 1 & 2)
        Arcs: see below
      Category 3 (Heuristic optimization): no fixed structure
(*) refers to the baseline configuration
Notes: For the first two cases, I have defined a set of cases of which I will compare the deltaV.
Constant: many combinations of arc lengths and intervals
Orbit-based: same idea but with arc interval based on LPF orbit period
For the heuristic approach has not predefined test cases, because that is what the optimization will give in the end and you don’t know such a config beforehand..
Note that one of the configurations is actually the baseline scenario.
NEXT SLIDE

## Slide 23: Category 1: Constant timing

## Slide 24: Candidate scenarios | Example, constant timing
Arc length: 1.0 day Arc interval: 3.0 day
Notes: If we look at the constant timing configurations, we can think of a configuration like this.

## Slide 25: Candidate scenarios | Example, constant timing
Arc length: 0.5 day Arc interval: 3.0 day
Notes: Same interval but shorter lengths

## Slide 26: Candidate scenarios | Example, constant timing
Arc length: 2.0 day Arc interval: 3.0 day
Notes: Same interval but longer lengths

## Slide 27: Candidate scenarios | Example, constant timing
Arc length: 1.0 day Arc interval: 1.0 day
Notes: Same lengths but shorter interval

## Slide 28: Results | Candidate scenarios | Constant
Arc length
Arc interval
    X-axis labels:
        Major x-axis: arc interval
        Minor x-axis: arc length
Notes: If these white bars are then extrapolated to one year we get these annual costs:
From the figure the following observations:
0.1, 0.2 day arc length is too short: not well enough able to estimate states accurately enough given the states
0.5 days arc length offers the best deltav for most interval cases. This means that the limiting factor is the arc length except for the tracking interval of 0.1 day.
deltav grows with increasing arc interval, which is because of the larger dispersion growth.
deltav larger for very small arc lengths. This is likely due to too overcorrections where the next correction is trying to compensate for the previous correction that hasn’t fully taking into effect yet
NEXT SLIDE

## Slide 29: Results | Candidate scenarios | Constant
    Largest impact caused by arc duration
    Little difference between 0.5 to 3.0 arc interval range
    Best annual 0.375 0.0020 1 m/s or (-38.5970.228 1 %)
Arc length
Arc interval
Notes: If these white bars are then extrapolated to one year we get these annual costs:
From the figure the following observations:
0.1, 0.2 day arc length is too short: not well enough able to estimate states accurately enough given the states
0.5 days arc length offers the best deltav for most interval cases. This means that the limiting factor is the arc length except for the tracking interval of 0.1 day.
deltav grows with increasing arc interval, which is because of the larger dispersion growth.
deltav larger for very small arc lengths. This is likely due to too overcorrections where the next correction is trying to compensate for the previous correction that hasn’t fully taking into effect yet
Compared to baseline scenario
Best: the 0.5-0.5 day arc length-interval combination with 0.375 m/s (-38.597%)
NEXT SLIDE

## Slide 30: Category 2: Orbit-based timing
Notes: The same thing plot can be made with the orbit-based case. We can vary the arc length and the interval in terms of the number of LPF orbits.

## Slide 31: Candidate scenarios | Example, orbit-based
Notes: Every 1 pass with 0.1 arc length

## Slide 32: Candidate scenarios | Example, orbit-based
Notes: Every 8 passes with 0.1 arc length

## Slide 33: Candidate scenarios | Example, orbit-based
Notes: Every 8 passes with 0.2 arc length

## Slide 34: Results | Candidate scenarios | Orbit-based
Arc length: 0.10 day
Arc length: 0.15 day
Arc length: 0.20 day
    Trends:
        Every 4-5 passes the best
        Larger interval = more uncertainty
        No clear trend at 0.15 and 0.20 days
Notes: Explain figure
For this timing category the trends across intervals is less clear. But:
Large spikes for 0.1-day perilune with larger interval
Larger uncertainty with increasing interval
tracking for every 4-5 periods is the most ideal.
NEXT SLIDE

## Slide 35: Results | Candidate scenarios | Orbit-based
    Trends:
        Every 4-5 passes the best
        Larger interval = more uncertainty
        No clear trend at 0.15 and 0.20 days
    Best annual
        Perilune: 0.505 0.0124 1 m/s
          -17.618%
        Apolune: 0.498 0.0082 1 m/s
          -18.760%
Arc length: 0.10 day
Arc length: 0.15 day
Arc length: 0.20 day
Notes: Compared to baseline:
Not many improvements
Best:
For 0.15 days of tracking (perilune: 6 days, apolune: 4 days)
NEXT SLIDE

## Slide 36: Best solutions thus far…
Notes: So far we have the following results. We can see that thusfar the best finding comes from the constant arc case.
NEXT SLIDE

## Slide 37: Category 3: Timing based on heuristic optimization
Notes: But can we make better reductions?
As mentioned before, the costs comes from a complex coupled dynamical system both in space and time:
Spatially, we are dealing with the estimation error that depends on the relative geometry during tracking
In terms of time, we know that a previous correction has a direct effect on the future trajectory that in turn affects the dispersion and OD process and ultimately the mag and dir of the next correction.
To solve this we make use of heuristic optimization methods.
NEXT SLIDE

## Slide 38: Results | Heuristic optimization
    Noisy and undifferentiable solution space
    High dimensionality (N arcs)
    Algorithm:
        Particle Swarm (PSO)
      Multiple solutions (5 total)
Notes: Reduce the ∆V objective by adjusting the length of each individual arc separately
Done by alpha, start with the baseline configuration
Multiple algorithms to be used but
Randomness involved with the range-observables,: noisy and non-diff design space.
Handle converge to solutions in high-dimensional spaces. PSO good solution for this.
“heuristic”:
solutions that are not guaranteed globally optimal but are sufficient
It is not possible to get only one solution (obs noise). As such I run the algorithm with different observation histories from the same noise distribution to generate a total of 5 solutions.
NEXT SLIDE
Reduce the ∆V objective by adjusting the length of each individual arc separately.
This will be done according to the scheme shown on the right in the slide. As you can see, the settings are the same as the baseline in the sense that its starts at MJD60390. It also keeps having an interval of 3 days and the annual costs are based on simulation of 28 days. The difference between the baseline case and this optimization routine is that each T_i, shown in the design vector alpha can have different values. The initial conditions starts at the baseline case as can been observed by the 1s in alpha0.
In order to solve this, not every algorithm can be used. Because there is randomness involved with the range-observables, the total deltav can be slightly different for the same design vector. As such, the design space is noisy and non-differentiable. Also, has to be able to converge to solutions in high-dimensional spaces. PSO good solution for this.
Lastly, “heuristic” implies that solutions that are not guaranteed to be globally optimal but are sufficient for reaching a solution that improves the total maneuver cost. Especially when there is observation noise involved, it is not possible to get only one solution. As such I run the algorithm with different observation histories from the same noise distribution to generate a total of 5 solutions.

## Slide 39: Results | Optimization analysis | PSO
    Best case of PSO optimization
    Best mean0.280 m/s (-54.18%)
    = [1.62, 1.14, 1.17, 0.10, 0.22, 0.10, 0.10]
Notes: This figure shows the best solution found for a PSO solution. Explain figure
It shows that there is even more room for improvement between the baseline and optimized solution. The base case yields a deltaV of 0.280 or a -54.18% change.
This solution offers some intuitive insights of the reasoning of what makes it a good solution.
NEXT SLIDE

## Slide 40: Results | Optimization analysis
      Longer arc at start:
        Better observability
        Prioritize early error reduction
      Short arcs at end:
        Lower observability
        Estimation error << dispersion error
    Shorter overall tracking in optimized case:
        Good news!
Notes: For example:
Longer tracking at start
This can be explained by a preference for lower estimation error as soon as possible. Can be seen by the lower value of estimation errors later.
An additional point related to this is the better state observability. It could also be that it is easier to perform OD for relative geometries that occur in the first 10 or so days.
2. Shorter tracking at start
This can be explained partially by the potentially worse observability at the end
Lower deltav explained by the fact that corrections take place earlier such that they occur at a lower dispersion.
Shorter total tracking: which is beneficial for good power budgets as well, will touch upon later.

## Slide 41: Optimized scenario | Layout
Notes: Visual of the orbit geometry comparing the cases.
NEXT SLIDE

## Slide 42: Results | Optimization analysis | PSO
    5 solutions total (range -47.46% to -54.18%) Solution details in appendix
Notes: Each run yielded a different design vector solution, all around -50%
All tendency to first reduce estimation error, smaller arcs later.
The full set of design vectors can be found in the appendix.
NEXT SLIDE

## Slide 43: Best solutions
Notes: But finally we have this overview
NEXT SLIDE

## Slide 44
Results
Design and operational considerations
Notes: We can reduce deltav over the lifetime of LUMIO under idealized circumstances. Meaning that we must also think about:
DeltaV for non-ideal scenarios due to subsystem limitations
How other design relevant parameters such as required power are affected.
NEXT SLIDE

## Slide 45: Propulsion system

## Slide 46: Results | Design considerations | Propulsion subsystem
      specifications of LUMIO propulsion subsystem:
        Minimum of 0.003 m/s
      Simulations:
        > 0.003 m/s not always true
* = assumed value based on the other
Notes: first subsystems GNC: propulsion system.
The Phase A study of LUMIO suggested the use of one two thrusters: NanoAvionics and Bradford-ECAPS
performance envelope affect deltav.
envelope of possible ∆V from minimum and maximum thrust levels as well as the burn time associated with the thrusters.
Minimal ∆V 0.003 m/s.
Most individual corrections of the optimized solution are above this value so it should be possible to use the given thrusters in real-life.
NEXT SLIDE

## Slide 47: Results | Design considerations | Propulsion subsystem
      specifications of LUMIO propulsion subsystem:
        Minimum of 0.003 m/s
      Effect on :
        Some increase:
          0.280 m/s to 0.510 m/s
        Optimization:
          More variation in results
          But can still yield improved costs in some cases
Based on optimized case with
= [1.62, 1.14, 1.17, 0.10, 0.22, 0.10, 0.10]
Notes: However, not all corrections are above 0.003 m/s in the solution. In the figure on the right, you can a small sensitivity analysis where the minimal deltav threshold varies.
The red bar represents the costs if we implement an actual LUMIO subsystem with the best optimized timing configuration. The lowest gray bar represents the costs associated with the best-found solution from the heuristic optimization shown below.
If this threshold included in the calculations, then an increase in deltaV 0.51 m/s: to larger deltav to compensate for mission deltav opportunity.
NEXT SLIDE

## Slide 48: Results | Design considerations | Propulsion subsystem
      specifications of LUMIO propulsion subsystem:
        Minimum of 0.003 m/s
      Effect on :
        Some increase:
          0.280 m/s to 0.510 m/s
        Optimization:
          More variation in results
          But can still yield improved costs in some cases
      What if 0.003 m/s threshold is included in the PSO optimization routine?
Based on optimized case with
= [1.62, 1.14, 1.17, 0.10, 0.22, 0.10, 0.10]
Notes: Again baseline for reference.
still an improvement, but less.
more variation in the results.
BUT:
Alpha from optimization with no threshold
the optimizer has to adjust for this design constraint and might find a solution that fits the specific settings better.
NEXT SLIDE

## Slide 49
      > 0.003 m/s
      > 0.000 m/s
Notes: If the deltav threshold is included PSO finds a different minimization solution with the additional constraint.
NEXT SLIDE

## Slide 50: Results | Design considerations | Propulsion subsystem
      Optimization solutions:
      More variation in results
      Still improved
      Less variation for longer duration
Notes: If we include the deltav threshold in the optimization process, we get the following results.
From the figure, the following observations can be made:
Including thruster limitations increases uncertainty
Optimizing using a longer time frame reduces the uncertainty although the costs are still larger than when there is no threshold. As such, longer timeframes more reliable estimate of the costs with a propulsion limit
Luckily, even solutions with subsystem limitations can still yield improvement over the baseline.
NEXT SLIDE
Both observations show that a shorter simulation time has a larger effect on the annual deltav.

## Slide 51: Power budget
Notes: Thusfar only deltav, but there are also other parameters that can be relevant to a mission such as the required power to perform OD and navigation related tasks.
NEXT SLIDE

## Slide 52: Results | Design considerations | Power budget
      Total tracking time affects power consumption
      Average power used to compare cases
Notes: To have an indication of the expected power over the mission due to the OD and navigation related tasks, I considered three subsystems that are most relevant. Based on this:
An ”average power” value is used.
The required power of the three components are weighted by the time fraction in which they are on or off compared to the total duration. This is to compare configs.
Since different tracking configurations have different total tracking times and different amounts of tracking arcs, their average power is different.
Consequently, for the mission design, this difference in power demand can affect how one allocates power on-board. This can lead to design changes and might lead to better scientific yield as a bit more power can be spent on instruments.
NEXT SLIDE

## Slide 53: Results | Design considerations | Power budget
      Total tracking time affects power consumption
      Average power used to compare cases
Notes: Given we bar chart:
Most power demand from transponder so tracking for longer has some effect on the average power usage.
NEXT SLIDE

## Slide 54: Results | Design considerations | Power budget
      Total tracking time affects power consumption
      Average power used to compare cases
      Power-Δ𝑉 trade-off
Notes: If compared to deltav,
Inverse relationship: trading better deltav against better power.
Heuristic case is a middle ground
NEXT SLIDE

## Slide 55: On-board dynamic model
Notes: The last part that I want to touch upon is the choice of the dynamic model that is used on-board. In other words, the choice of the physical environment that is used to calculate the estimations and corrections on-board LUMIO.
Run time affects to delay correction calculation
Dispersion affects magnitude of correction
NEXT SLIDE
Used to calculate the corrections which requires a propagation of a trajectory a few days into the future.
Running this takes time, which can affect how much delay there will be between the time of the last known estimated state and the actual correction. This can affect how accurate the correction is and ultimately the magnitude of the total deltaV.

## Slide 56: Results | Choice of on-board dynamic model
Details on dynamic models in appendix
    Run time:
        More complex = longer
        Large range (LUMIO OBC)
          ~35 to 8800 sec (1 day)
          PMSRP01: 528 sec
        Run time still small compared to LUMIO’s 12h cut-off
        Conclusion: orbit propagations are easily done on-board
Notes: Let first start with the run times.
On the x-axis you can see the different types of models. While I won’t go into details of these, the dynamical complexity grows as we go to the right. In short, PM refers to models in which celestial bodies are point masses, SH are models that include spherical harmonics instead and those that have SRP include the additional force due to solar radiation pressure. Details of the models can be found in the appendix of the report.
Clearly, it takes longer to run complex models, orders to magnitude longer, ranging from 0.8 s to 200 sec. Note that the figure shows the results using the CPU of my laptop with a frequency of 2.2GHz. If we consider the OBC of LUMIO (frequency 44 times smaller), leads to range of 35 to 8800 sec.
This suggest that there are some models that are substantially worse than other. However, even the worst case is negligible compared to the 12h cutoff time currently used.
NEXT SLIDE

## Slide 57: Results | Choice of on-board dynamic model
    Run time:
        More complex = longer
        Large range (LUMIO OBC)
          ~35 to 8800 sec (1 day)
          PMSRP: 528 sec (TPM)
      Dispersion:
        SRP yields improvement
        SH instead of PM makes little difference
        PMSRP1 best choice
        LUMIO OBC can still be used
Details on dynamic models in appendix
Notes: For dispersion we see the opposite trend
The simplest dynamic model yields order of magnitude higher error, circular orbit around the moon.
SRP reduces the error.
We also see that spherical harmonics don’t have much of an influence. Saves time to use PM.
More planetary bodies little effect.
PMSRP01 was chosen (This is just the PM of Earth, Moon and Sun with SRP)
PM-type models are shorter in terms of run time
including SRP yields a drastic effect on the dispersion
With this model and LUMIO’s current OBC it takes 528 seconds for a 3-day TPM calculation.
10 minutes small compared to 12 h, the current OBC can still be used in the design.
NEXT SLIDE

## Slide 58: Results | Choice of on-board dynamic model
    Run time:
        More complex = longer
        Large range (LUMIO OBC)
          ~35 to 8800 sec (1 day)
          Still small (12h cut-off)
      Dispersion:
        CRTBP worst
        SRP yields improvement
        SH instead of PM makes little difference
        PMSRP1 chosen in this work
Details on dynamic models in appendix
Notes: But run time is not the only factor.
Dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, is also important to deltav.
In the figure, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Since we know that the PM-type models are shorter in terms of run time and including SRP yields a drastic effect on the dispersion, PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.
All in all, this model requires 528 seconds for a 3-day TPM calculation. Because the dispersion won’t grow in 10 minutes, the current OBC can still be used in the design.

## Slide 59
Closing remarks

## Slide 60
Research question
What is an optimal satellite-to-satellite tracking timing configuration for cislunar orbiters?
Notes: While the degree of succes depends on the type of timing strategy category we use, it was shown that improvements can be made over the baseline scenario in each category.
To recap, in this work I have shown that:
Possible to substantially reduce the deltaV budget.
Timing scheduling is a beneficial spacecraft design consideration that can be used for a cislunar mission that performs autonomous orbit determination and navigation.

## Slide 61: Concluding remarks | Research benefits
    Timing scheduling is a beneficial spacecraft design consideration
    Dynamic model
        PM+SRP works best
      Timing solutions
        Constant configuration: best case 0.375 m/s (-38%)
        Optimization algorithms: best case 0.294 m/s (-52%)
      Sensitivity analysis
        Similar cost for other start date
        Propulsion system specs have significant effect
More scientific yield
Rationale:
Extended operational phase due to fuel savings
Overall shorter tracking time: more power to payload
Navigation of lunar assets on inaccessible places
Lower operational and design costs
Rationale:
No need for expensive Earth-based orbit determination (not limited to SmallSats)
Use existing COTS products
Applicable to existing subsystems
Rationale:
With LUMIO’s thruster specs still reduction
LUMIO’s OBC sufficient run time dynamic model
So no major design changes for LUMIO (OBC, thruster, transponder)
Notes: As a recap to the research reiterate the following contributions
1. More availability for scientific goals
Extended operational phase due to fuel savings
Overall shorter tracking time: more power to payload
Navigation of lunar assets on inaccessible places
2. Extended mission duration
LUMIO’s OBC sufficient run time dynamic model
With LUMIO’s thruster specs still reduction
So no major design changes for LUMIO (OBC, thruster)
3. Applicability with existing propulsion systems
No need for expensive Earth-based orbit determination (not limited to SmallSats)
Use existing COTS products

## Slide 62: Concluding remarks | Recommendations
Increase model
realism
Rationale:
Both spacecraft have own science objectives, no availability
Limited inter-satellite distance due to power constraints and pointing errors
Estimate bias and other model parameters
Increase representable period to longer periods
Evaluate other orbit geometries
Rationale:
Relative geometries are different
Station keeping can act different
Include automatic decision making
Rationale:
Now planning beforehand
Live adjustments in case of malfunctions, collision avoidance, etc.
Notes: Finally, other aspects future research
1. Increase model realism
Both spacecraft have own science objectives, no availability
Limited inter-satellite distance due to power constraints and pointing errors
Estimate bias and other model parameters
Increase representable period to longer periods
2. Evaluate other orbit geometries
Relative geometries are different
Station keeping can act different
3. Include automatic decision making
Now planning beforehand
Life adjustments in case of malfunctions, collision avoidance, etc.

## Slide 63
Thank you for your attention
Questions?

## Slide 64
Appendix

## Slide 65
Appendix
Crosslink radiometric orbit determination

## Slide 66: Methodology | Nomenclature
    Measurements:
        Range-only
    Three types of trajectories:
        Truth: actual trajectory
        Estimated: approximation of the truth using ISL observations
        Reference: path that show be followed
Notes: Before I go more into the details, it is important to establish a naming convention. It is important to keep in mind that we will be doing both OD and navigation.
range-only, so we are using relative distance information during orbit determination.
For OD, want to know the true orbit. The true orbit is never known, but depending on where, how often, and how accurately we measure the inter-satellite distance: estimated orbit
Based on the best knowledge we have of the truth; we will perform station keeping correction. But to know how to perform these corrections, we need to know with trajectory we need to follow. I will call this the reference trajectory.
NEXT SLIDE

## Slide 67
Definition
“Crosslink radiometric orbit determination”
“The estimation of the absolute position and velocity of at least two spacecraft using only radiometric inter-satellite observables.”
Notes: Before I go to

## Slide 68
    Estimation:
    Approximating the true position and velocity based on measurements
    Accuracy of position and velocity depends on observational geometry
    Coupled relationship between states of involved spacecraft
    Different algorithms:
        Sequential and batch-wise
“The estimation of the absolute position and velocity of at least two spacecraft using only radiometric inter-satellite observables.”

## Slide 69
“The estimation of the absolute position and velocity of at least two spacecraft using only radiometric inter-satellite observables.”
    Batch Least Squares (BLS) estimation algorithm
    Measurements obtained in tracking arcs/batches
    Estimation accuracy relies on observability:
        Observable type (range-only)
        Relative orbits satellites
        Amount of measurements
        Initial state information (a-priori covariance)
        Degree to which orbit is perturbed by other forces (acceleration asymmetry)

## Slide 70
    Batch Least Squares (BLS) estimation algorithm
    Measurements obtained in tracking arcs/batches
    Estimation accuracy relies on observability:
        Observable type (range-only)
        Relative orbits satellites
        Amount of measurements
        Initial state information (a-priori covariance)
        Degree to which orbit is perturbed by other forces (acceleration asymmetry)
“The estimation of the absolute position and velocity of at least two spacecraft using only radiometric inter-satellite observables.”
Notes: In general, relative observations alone are not sufficient to provide a unique OD solution. In a completely symmetric acceleration field, there are infinite combinations of orbits that can result in the same SST observation history. However, an asymmetric acceleration field results in a unique time history of SST observations. Given adequate asymmetry in the acceleration field, LiAISON is able to converge on a unique OD solution.

## Slide 71
    Batch Least Squares (BLS) estimation algorithm
    Measurements obtained in tracking arcs/batches
    Estimation accuracy relies on observability:
        Observable type (range-only)
        Relative orbits satellites
        Amount of measurements
        Initial state information (a-priori covariance)
        Degree to which orbit is perturbed by other forces (acceleration asymmetry)
“The estimation of the absolute position and velocity of at least two spacecraft using only radiometric inter-satellite observables.”
Notes: In general, relative observations alone are not sufficient to provide a unique OD solution. In a completely symmetric acceleration field, there are infinite combinations of orbits that can result in the same SST observation history. However, an asymmetric acceleration field results in a unique time history of SST observations. Given adequate asymmetry in the acceleration field, LiAISON is able to converge on a unique OD solution.

## Slide 72
    Absolute position and velocity :
    Position and velocity w.r.t. a central body (Earth)
    Not all observations can provide absolute information
        Depends on concept of observability state estimation process
“The estimation of the absolute position and velocity of at least two spacecraft using only radiometric inter-satellite observables.”

## Slide 73
    Radiometric inter-satellite observables
    Two-way range only
“The estimation of the absolute position and velocity of at least two spacecraft using only radiometric inter-satellite observables.”

## Slide 74
Appendix
Assumptions

## Slide 75: Methodology | assumptions
    Assumption 1: 28 instead of 365 days
    Assumption 2: After 14 days “representable period”
    Assumption 3: Instantaneous corrections after arc
    Assumption 4: Monte Carlo for cost variations: error bars
    Annual approximation by scaling:
Notes: Due to the complex nature of the problem, I will address some aspects that I took into consideration when performing the calculations on ∆V.
As you may have noticed, the simulation duration is 28 days. However, I said earlier that we want to know the ∆V associated with 1 year of LUMIO operations. The simple reason for this are the computational limitations when running the simulation where it takes too long and memory to perform proper analysis. The 28-day duration covers two full LUMIO orbital periods which was deemed sufficient to represent costs for the full mission duration.
Another assumption is that in order to remove effects coming from orbit insertion and to have a stable nominal navigation scenario, only the corrections after 14 days since the mission start epoch are counted towards the annual cost approximation.
I also assumed that the corrections happen instantaneously after OD, meaning that the thruster or pointed directly in the right direction and that the time to calculate the right SKM is negligible small compared to the length of a tracking arc.
Lastly, ∆V costs are of a stochastic nature due to varying measurement noise histories in the estimation process, so ∆V is always based on Monte Carlo runs of the orbit estimation and navigation process, such that the cost estimates are defined by a mean and standard deviations as indicated by the error bars in the figure.

## Slide 76
Appendix
Model details

## Slide 77: Methodology | On-board dynamic model
    Dynamical environment affects the orbit corrections
    High-fidelity:
        Longer run, more accurate
      Low-fidelity:
        Short run, less accurate
    Which one to choose?
Details in the appendix
Notes: One important part of the simulation that I want to highlight is the choice of the dynamic model.
In other words, the choice of the physical environment that is used to calculate the estimation and corrections on-board LUMIO. Adding more force terms, such as the gravitational effect of other planets or the imperfections of the gravitational field the Earth and Moon (SH) or the inertia generated from the solar radiation (SRP), does improve realism but it comes at the cost of more resources.
Because of this, I will do an analysis where I compare the run time and the closeness or dispersion with the reference orbit from Polimi.
I have categorized models in three parts from simple to complex:
LF assumes the easiest model to make the L2 orbit, which is just a point mass of Earth and Moon without any other perturbations, which leads to perfectly circular orbit of the Moon around Earth.
HF includes the effect of other planetary bodies and imperfections of gravity of Earth and Moon
FF yields the more complex model, where all possible force terms that tudatpy offers are used, such as relativistic effects and SRP because of the albedo from the Moon.

## Slide 78: Dynamic model details

## Slide 79: Other model details

## Slide 80
Appendix
Optimization model tests

## Slide 81: Results | Optimization analysis | Different settings
    Running optimization routine with different settings
    Can affect final solution/
All optimization solutions are in the appendix
Notes:     ONLY IF ENOUGH TIME LEFT, SKIP TO NEXT CHAPTER
    Because the solution could be different with different model settings, I also looked at how the optimization solution would be affected.
    Variety of scenarios are tested:
    Algorithm: concerned about how well it can converge a solution. Able to handle high dims and noise?
    Model duration: concerns also about high dim double states, is 28 as representable for annual cost as 56 days?
    Model fidelity: does complex dynamic model different results as it can affect the dispersion?
    While the exact solutions can be found in the appendix
    NEXT SLIDE

## Slide 82: Results | Optimization analysis | Nelder-Mead
    Best case of Nelder-Mead optimization
    Best mean0.422 m/s (-30.93%)
    = [1.13, 1.01, 0.90, 0.81, 0.93, 0.89, 0.83]
Notes: Lets first look at how the Nelder-Mead algorithm compares to the earlier shown PSO.
Clearly, there is little change between the baseline and optimized solution. The base case yields a deltaV of 0.4224 or a -30.93% change
However clearly, better results can be made with the PSO.
NEXT SLIDE

## Slide 83: Results | Optimization analysis | Comparison
Notes:     But does this also happen across all runs, yes! Between the PSO and Nelder-Mead you can clearly see that PSO configurations yield better results. Nonetheless, other optimization algorithms also can yield cost reductions of the baseline as shown in red.
    If we now compare the solutions of the PSO algorithm to the other test cases on model fidelity and duration we get the following results:
    NEXT SLIDE

## Slide 84: Results | Optimization analysis | Comparison
    Overall improvement w.r.t. baseline configuration
    Simulating for shorter duration might underestimate actual costs
    PMSRP yields similar costs as SHSRP
Notes: We see that running for a larger design space does yield larger costs. At first it was no convergence, larger dim, but convergesd. Then it be because the 28 days case does not serve as a presentive period for the year.
Another point is that PMSRP yields similar costs as SHSRP which validates that using a more simple model with point masses can give optimized results that can yield the same order of cost improvemens.
From the comparison clearly all cases perform better than the baseline.
NEXT SLIDE

## Slide 85
Appendix
Details navigation model

## Slide 86: Methodology | Overview simulation setup
Notes: In order to actually get to the final deltaV, there is a complex coupled simulation structure that comes before.
The model exists out of multiple models, which all do different things. While I don’t have the time to go into detail, a few things are important to remember:
The most important input is the tracking arc configuration, or observation widows, which define the relative geometries at which tracking and maneuvers occur.
We have three types of trajectories. The orbit estimation estimates the true states (where there are estimation errors) and the true state can be in a place where it shouldn’t be compared to the reference trajectory (called dispersion). These two trajectory errors affect the SKMs calculated by a correction model.
After a SKM is performed, it affects the true path of the spacecraft, which in turn affects the estimation process and thus the accuracy of the next correction.
This is at the core of what make this a complex optimization problem.
Finally, the truth and estimated orbit are calculated in a predefined physical environment. The choice of the environment affects how well the estimated orbit matches truth and reference orbit and thus the affects the total deltav.
NEXT SLIDE

## Slide 87: Methodology | Simulation layout: Target Point Method (TPM)
    Assumptions
        1 TP
        3 days downstream
        No cut-off duration
      Dependencies
        Location tracking arc (orbit geometry)
        Dispersion (difference from reference)

## Slide 88: Methodology | Correction model
    Target Point Method (TPM)
        Using 1 TP, 3 days downstream
        OD campaign = tracking arc
        No cut-off duration

## Slide 89: Methodology | Navigation model

## Slide 90: Methodology | External Resources
    Tudatpy astrodynamics toolbox
    Used for
    Orbit propagation
    Orbit determination
    LUMIO reference trajectory
    Used for
    Orbit corrections
Notes: Two external resources are used
Most are important in their own way
Tudatpy is an open-source python package used for everything related to astrodynamics and is a preferred choice for many courses within the faculty already as it is developed by TU Delft.
TU Delft works closely with Polimi on the LUMIO project. They have originally designed the reference trajectory that LUMIO should follow. Their data was been used to calculate the correction manoeuvres.

## Slide 91
Appendix
Sensitivity analysis
Notes: Before I go to the concluding remarks, I will show the results of the sensitivity analysis. The navigation model contains a variety of parameters that could be adjusted. This means that any adaptation to those variables comes with a degree of variability of the ∆V objective outcomes. This section evaluates the sensitivity of those outcomes to these variable changes.

## Slide 92: Sensitivity analysis | Observation window parameters
    Baseline settings, only parameter change only
    Main take-aways:
        Arcs length of 0.5 day performs best
        Shorter interval is better
        Lower sensitivity to start epoch
          Analysis is representative when starting at different orbit locations
Notes: The first two parameters, arc length and arc interval are technically already covered by the constant timing category results.
An arc duration of 0.1 days seems to provide the least ideal ∆V . A possible explanation for this could be that consistently for 0.1 days might not be enough to capture sufficient useful observational geometry which causes the estimation error to remain relatively large over time. On the other hand, at some point, tracking for too long allows for dispersion to grow in the meanwhile and the trade-off between improved estimation error does not outweigh the benefits of a SKM at a lower dispersion. Also, note the larger standard deviation values for the shortest arc. This could be explained by a larger difference in estimation outcomes due to a lower number of measurements for those shorter arcs. This gives more variation in the estimation errors. As a result, the final BLS outcome of the initial states might vary more

## Slide 93: Sensitivity analysis | Observation window parameters
    Baseline settings, only parameter change only
    Main take-aways:
        Arcs length of 0.5 day performs best
        Shorter interval is better
        Lower sensitivity to start epoch
          Analysis is representative when starting at different orbit locations

## Slide 94: Sensitivity analysis | Auxiliary parameters
    Main take-aways:
        Annual costs not influenced by initial errors
        Insensitivity to obs. noise and frequency
        Target points:
          Smallest at 3-4 days
        Minimal threshold high
      Details in appendix slides
Notes: Most notably, the total cost is not much affected by the initial values of estimation error unless both the position and velocity components are increased by tenfold. However, the stable period after 14 days remains the same. Likewise, this is the case for varying insertion errors. This validates the notion that after 14 days, one has reached the stable region for nominal operation and the SKMs cost is just affected by the choice of observation windows.

## Slide 95: Sensitivity analysis | Auxiliary parameters
    Main take-aways:
        Annual costs not influenced by initial errors
        Insensitivity to obs. noise and frequency
        Target points:
          Smallest at 3-4 days
        Minimal threshold high
      Details in appendix slides

## Slide 96
Appendix
LPF-LUMIO Case study

## Slide 97: Scientific context | LUMIO-LPF case study
Notes: Here is visual representation to give you a better sense of the orbital geometries. Blue is the LPO, red the ELO. In the inertial frame, you can see the small orbit of LPF orbiting the Moon and the blue LUMIO orbit always moving further from Earth than the Moon itself.
The other figures show the same orbits but described in the non-dimensional synodic frame, which means that the x axis is aligned with the Earth-Moon distance. This makes it easier to see how the satellites move w.r.t each other.
You can see that LUMIO always covers up and down behind the Moon from the perspective of Moon and thus LPF. You can also see that the orbit of LPF is much smaller and covers a lot of the 3D volume. In short, this allows for many vantage points between the satellites.

## Slide 98: Scientific context | LUMIO-LPF case study
Notes: You saw that the structure is still maintained, but gravitational pulls and other perbutational forces eventually distort its quasi-periodic structure. It clearly shows the need for a set of corrective manoeuvres within a (28-day period) to be able to sustain the periodic structure.

## Slide 99: Scientific context | LUMIO-LPF case study
Notes: If we do this correctly, 1 year of operations looks like this, where LUMIO maintains within this torus-shaped structure.

## Slide 100
Appendix
Details baseline scenario

## Slide 101: Results | Default scenario | State estimation uncertainty

## Slide 102: Results | Default scenario | State estimation uncertainty

## Slide 103: Results | Default scenario | Estimation error

## Slide 104: Results | Default scenario | Dispersion

## Slide 105: Results | Default scenario | Dispersion

## Slide 106: Results | Default scenario | Observations

## Slide 107: Results | Default scenario | State correlations

## Slide 108: Results | Default scenario | Observability

## Slide 109
Appendix
Sensitivity analysis
Observation window parameters

## Slide 110
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 111
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 112
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 113
Appendix
Sensitivity analysis
Auxiliary parameters

## Slide 114
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 115
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 116
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 117
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 118
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 119
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 120
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 121
Appendix
Optimization result tables

## Slide 122: Results | Optimization anaysis
    Nelder-Mead, 28 days, PMSRP dynamic model
Notes: One important aspect to show is how the optimization model works.
Here you can see the problem definition that will be used. The start epoch is at MJD60390. The design vector only contains values for the arc lengths, which are initially defined with a length of 1. Also, a constant interval is 3 days is used. As such, the initial condition signifies the baseline scenario.
It should be noted that there is a level of randomness occurring the optimization process. This is caused by the measurement noise, which gives different estimates, which consequently results in slightly different delta_v values. To add to this, one should note that the magnitude and direction of a correction is a direct result of the previous correction.
This means that we look for an optimization algorithm that can handle noisy design space and does not require gradient information. In my work I used two heuristic optimization algorithms: The Nelder-Mead & PSO.

## Slide 123: Results | Optimization anaysis
    PSO, 28 days, PMSRP dynamic model
Notes: One important aspect to show is how the optimization model works.
Here you can see the problem definition that will be used. The start epoch is at MJD60390. The design vector only contains values for the arc lengths, which are initially defined with a length of 1. Also, a constant interval is 3 days is used. As such, the initial condition signifies the baseline scenario.
It should be noted that there is a level of randomness occurring the optimization process. This is caused by the measurement noise, which gives different estimates, which consequently results in slightly different delta_v values. To add to this, one should note that the magnitude and direction of a correction is a direct result of the previous correction.
This means that we look for an optimization algorithm that can handle noisy design space and does not require gradient information. In my work I used two heuristic optimization algorithms: The Nelder-Mead & PSO.

## Slide 124: Results | Optimization anaysis
    PSO, 28 days, SHSRP dynamic model
Notes: One important aspect to show is how the optimization model works.
Here you can see the problem definition that will be used. The start epoch is at MJD60390. The design vector only contains values for the arc lengths, which are initially defined with a length of 1. Also, a constant interval is 3 days is used. As such, the initial condition signifies the baseline scenario.
It should be noted that there is a level of randomness occurring the optimization process. This is caused by the measurement noise, which gives different estimates, which consequently results in slightly different delta_v values. To add to this, one should note that the magnitude and direction of a correction is a direct result of the previous correction.
This means that we look for an optimization algorithm that can handle noisy design space and does not require gradient information. In my work I used two heuristic optimization algorithms: The Nelder-Mead & PSO.

## Slide 125: Results | Optimization anaysis
    PSO, 56 days, SHSRP dynamic model
Notes: One important aspect to show is how the optimization model works.
Here you can see the problem definition that will be used. The start epoch is at MJD60390. The design vector only contains values for the arc lengths, which are initially defined with a length of 1. Also, a constant interval is 3 days is used. As such, the initial condition signifies the baseline scenario.
It should be noted that there is a level of randomness occurring the optimization process. This is caused by the measurement noise, which gives different estimates, which consequently results in slightly different delta_v values. To add to this, one should note that the magnitude and direction of a correction is a direct result of the previous correction.
This means that we look for an optimization algorithm that can handle noisy design space and does not require gradient information. In my work I used two heuristic optimization algorithms: The Nelder-Mead & PSO.

## Slide 126: Results | Optimization anaysis
    PSO, 28 days, PMSRP dynamic model, with 0.003 m/s threshold
Notes: One important aspect to show is how the optimization model works.
Here you can see the problem definition that will be used. The start epoch is at MJD60390. The design vector only contains values for the arc lengths, which are initially defined with a length of 1. Also, a constant interval is 3 days is used. As such, the initial condition signifies the baseline scenario.
It should be noted that there is a level of randomness occurring the optimization process. This is caused by the measurement noise, which gives different estimates, which consequently results in slightly different delta_v values. To add to this, one should note that the magnitude and direction of a correction is a direct result of the previous correction.
This means that we look for an optimization algorithm that can handle noisy design space and does not require gradient information. In my work I used two heuristic optimization algorithms: The Nelder-Mead & PSO.

## Slide 127: Results | Optimization anaysis
    PSO, 56 days, PMSRP dynamic model, with 0.003 m/s threshold
Notes: One important aspect to show is how the optimization model works.
Here you can see the problem definition that will be used. The start epoch is at MJD60390. The design vector only contains values for the arc lengths, which are initially defined with a length of 1. Also, a constant interval is 3 days is used. As such, the initial condition signifies the baseline scenario.
It should be noted that there is a level of randomness occurring the optimization process. This is caused by the measurement noise, which gives different estimates, which consequently results in slightly different delta_v values. To add to this, one should note that the magnitude and direction of a correction is a direct result of the previous correction.
This means that we look for an optimization algorithm that can handle noisy design space and does not require gradient information. In my work I used two heuristic optimization algorithms: The Nelder-Mead & PSO.

## Slide 128
Appendix
Dynamic models

## Slide 129: Acceleration terms
    More details in report
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 130: Acceleration terms
    More details in report
Notes: If we now look at dispersion, aka the error between LUMIO’s trajectory calculated on-board and its reference trajectory, we see first some obvious results. The simplest dynamic model yields order of magnitude higher error, explained by the circular orbit around the moon. Next, we see that including SRP improves the error. We also see that spherical harmonics don’t have much of an influence. This means that we can save a lot of time by using point masses instead. Same for FF. Finally, including the gravity effects of more planetary bodies has little effect.
Because of this, the PMSRP01 was chosen. This is just the PM of Earth, Moon and Sun with SRP.

## Slide 131
Appendix
Validation navigation model

## Slide 132: Validation navigation model
LUMIO’s current SKM scheme: 7, 7, 14 days

## Slide 136: Validation navigation model
Found annual 15.8 2.2 1 m/s
Close to literature findings (shown in mean+std)

## Slide 137
Appendix
Candidate scenario details

## Slide 138: Candidate scenarios | Constant
    Relationship between estimation, dispersion and corrections for varying arc durations (0.1 day to 2.0 day)
    Shorter tracking arcs = more cost uncertainty
    Larger dispersion = larger costs
Notes: Move to appendix